## Slide 1
Process Control: Designing Process and Control Systems for Dynamic Performance
Chapter 21. Multiloop Control: Performance Analysis
Copyright © Thomas Marlin 2013
The copyright holder provides a royalty-free license for use of this material at non-profit educational institutions

## Slide 2
CHAPTER 21: Multiloop Control Performance
When I complete this chapter, I want to be
able to do the following.
Distinguish favorable and unfavorable interaction
Balance controllability, integrity and dynamic performance
Apply two methods for decoupling
Properly select applications for decoupling

## Slide 3
Outline of the lesson.
Some observations on multiloop design performance
The RDG, Relative Disturbance Gain
Controllability and interaction
Disturbance directionality
Decoupling
CHAPTER 21: Multiloop Control Performance

## Slide 4
REQUIRED: DOF, Controllability, Operating Window
HIGHLY DESIRED
Integrity - Performance is “acceptable after one or more controllers become inactive
Control performance
- CVs achieve zero offset and low deviations from SP
- MVs have acceptable dynamic variability
Robustness - Performance (not just stability) is achieved for a range of plant dynamics
Range - Strong effect to compensate large disturbances
MULTILOOP CONTROL PERFORMANCE
Let’s learn how to achieve these
good properties

## Slide 5
MULTILOOP CONTROL PERFORMANCE
Motivating Example
No. 1 - Blending
FA, xA
FS, xAS = 0
FM, xAM
Must retune when flow controller is in manual!
The design with RGA nearer 1.0 is better

## Slide 6
MULTILOOP CONTROL PERFORMANCE
Motivating Example No. 2 - Distillation SP Response
FR  XD
FRB  XB
FD  XD
FRB  XB
RGA = 6.09
RGA = 0.39
For set point response, RGA closer to 1.0 is better

## Slide 7
MULTILOOP CONTROL PERFORMANCE
Motivating Example No. 3 - Distillation disturb. Response
FR  XD
FRB  XB
FD  XD
FRB  XB
RGA = 6.09
RGA = 0.39
For set point response, RGA farther from 1.0 is better

## Slide 8
MULTILOOP CONTROL PERFORMANCE
Conclusion from examples - RGA Alone does not provide sufficient information for control design
Key missing information is disturbance type
Key factor is the DISTURBANCE DIRECTION
Disturbances in this direction are easily corrected.
Disturbances in this direction are difficult to correct.

## Slide 9
MULTILOOP CONTROL PERFORMANCE
Short-cut Measure of Multiloop Control Performance
We want to predict the performance using limited information and calculations
We would like to have the following features
- Dimensionless
- Based on process characteristics
- Related to the disturbances type
Let’s recall if the RGA
had these features

## Slide 10
MULTILOOP CONTROL PERFORMANCE
Single-loop performance (dead times, large disturbances, etc. are bad)
Tune Factor
Change in tuning for multi-loop
Relative Disturbance Gain
dimensionless
only s-s gains
can be +/- and > or < 1.0
different for each disturbance
Usually the dominant term for interaction

## Slide 11
MULTILOOP CONTROL PERFORMANCE
What is this term?
What unique information is here?
What is the typical range?
Relative disturbance gain

## Slide 12
MULTILOOP CONTROL PERFORMANCE
Process Example: Binary Distillation with XD=.98, XB = 0.02
1. Calculate the RGA, RDG, ftune, and Ratio of integral errors for both loop pairings
2. Select best loop pairings
FR  XD
FRB  XB
FD  XD
FRB  XB
Energy Balance:
Material Balance:

## Slide 13
MULTILOOP CONTROL PERFORMANCE
Distillation tower (R,V) with both controllers in automatic for feed composition disturbance
Good performance in spite of the large RGA
XD XB

## Slide 14
MULTILOOP CONTROL PERFORMANCE
Distillation tower (R,V) with only XD controller in automatic for feed composition disturbance
Favorable interaction results in small XB deviation although it is not controlled!
No control!
XD XB

## Slide 15
Distillation Tower (R,V) with only XD controller in automatic and disturbance through FR model
MULTILOOP CONTROL PERFORMANCE
Example is change in reflux subcooling.
Good performance in spite of the large RGA
No control!
XD XB

## Slide 16
MULTILOOP CONTROL PERFORMANCE
PRELIMINARY LOOP PAIRING GUIDELINE
Pair loops with good single-loop performance and favorable interaction, as indicated by a small |RDG|.
Small = good SL performance
Small = favorable interaction

## Slide 17
MULTILOOP CONTROL PERFORMANCE
TAKING ADVANTAGE OF THE DYNAMICS
If unfavorable interaction exists in the best loop pairing, the effects of interaction can be reduced by tight tuning of the important loop and loose tuning of the less important loops.
FR  XD
FRB  XB
RGA = 6.09
Tightly
tuned
Loosely
tuned

## Slide 18
MULTILOOP CONTROL PERFORMANCE
TAKING ADVANTAGE OF THE DYNAMICS
Seek MV-CV pairings that provide fast feedback control for the more important loops. This tends to match the dynamic performance with the control objectives.
Evaluate the loop pairing for this process example, which supplies gas to a consumer from two sources.
PC
AC
E-1
P-1
P-2
V-1
vaporizer
gas
gas
A = composition

## Slide 19
MULTILOOP CONTROL PERFORMANCE
PROVIDING LARGE RANGE (OPERATING WINDOW)
For most important CVs, select an MV with large range.
- If other loops are in manual, the important loop retains large operating window.
Provide “extra” MV using split range capabilities.
AC
AC
Discuss the range available when
1. Both loops are in automatic.
2. Only one loop is in automatic.

## Slide 20
MULTILOOP CONTROL PERFORMANCE
PROVIDING INTEGRITY
Favor loop pairings with positive relative gains.
- Only use negative RGA if very advantageous dynamics
- Use zero RGA very carefully for dynamic advantage
If non-positive RGA used, add monitor to alarm operator when other loop is inactive
Consider the effects of RGA on tuning. Avoid high multiloop gains that lead to unstable single-loop systems.

## Slide 21
MULTILOOP CONTROL PERFORMANCE
RETAINING CONTROLLABILITY
Do not implement a loop that eliminates the causal relationship of another loop.
T
A
Reactant
Solvent
Coolant
Evaluate the design, specifically the control of the concentration in the reactor
Suggest an alternative design

## Slide 22
MULTILOOP CONTROL PERFORMANCE
RETAINING CONTROLLABILITY
Do not control the same variable with two loops with the same set point.
PC
Flows into the pipe
Flows exiting the pipe
PC
What problems could occur if the two PCs had the same set point?
Why would we use different set points?
Would the system function with different set points?

## Slide 23
MULTILOOP CONTROL PERFORMANCE
REDUCING EFFECTS OF DISTURBANCES
Implement loops that reduce the effects of disturbances before they affect the key controlled variables.
T
A
Reactant
Solvent
Coolant
How does this design satisfy the rule above.
Suggest additional methods for reducing the effects of disturbances

## Slide 24
MULTILOOP CONTROL PERFORMANCE
REDUCING THE EFFECTS OF UNFAVORABLE INTERACTION USING DECOUPLING
Retains the single-loop control algorithms
Reduces (eliminates) the effects of interaction
Three approaches
- Implicit decoupling: Calculated MVs
- Implicit decoupling: Calculated CVs
- Explicit decoupling: Controller compensation

## Slide 25
MULTILOOP CONTROL PERFORMANCE
IMPLICIT DECOUPLING: CALCULATED MVs
How can we adjust these calculated variables?
Are there any special tuning guidelines?

## Slide 26
MULTILOOP CONTROL PERFORMANCE
IMPLICIT DECOUPLING: CALCULATED CVs
How can we control these calculated variables?
Are there any special tuning guidelines?

## Slide 27
MULTILOOP CONTROL PERFORMANCE
+
-
+
+
+
+
-
+
Gc1(s)
Gc2(s)
G11(s)
G21(s)
G12(s)
G22(s)
Gd2(s)
Gd1(s)
D(s)
CV1(s)
CV2(s)
MV2(s)
MV1(s)
SP1(s)
SP2(s)
GD21(s)
GD12(s)
+
+
REDUCING THE EFFECTS OF UNFAVORABLE INTERACTION USING EXPLICIT DECOUPLING
Compensates for the effects of interaction

## Slide 28
MULTILOOP CONTROL PERFORMANCE
Decoupling - Perfect decoupling compensates for interactions
One design approach:
+
-
+
+
+
+
-
+
Gc1(s)
Gc2(s)
G11(s)/11
G22(s)/22
Gd2(s)
Gd1(s)
D(s)
CV1(s)
CV2(s)
SP1(s)
SP2(s)

## Slide 29
MULTILOOP CONTROL PERFORMANCE
Decoupling - Deciding when to decouple

## Slide 30
MULTILOOP CONTROL PERFORMANCE
FR  XD
FRB  XB
Which decoupling do you recommend?

## Slide 31
MULTILOOP CONTROL PERFORMANCE
Simulation confirms that top-to-bottom decoupling improves XB control performance.
|RDG*ftune | > 1.0
improvement

## Slide 32
MULTILOOP CONTROL PERFORMANCE
Simulation confirms that bottom-to-top decoupling does not improve XD control performance.
|RDG*ftune | < 1.0
No improvement
(a bit worse)

## Slide 33
MULTILOOP CONTROL PERFORMANCE
Decoupling - A large relative gain indicates extreme sensitivity to modelling errors can occur
(Worst case mismatch)

## Slide 34
MULTILOOP CONTROL PERFORMANCE
Decoupler with no errors; excellent performance!
Decoupler with 15% gain errors, unstable!
Decoupler performance can be very sensitive to gain errors. If possible, use process knowledge in determining plant gains, Kij.

## Slide 35
MULTILOOP CONTROL PERFORMANCE
Decoupling
Because the closed-loop system changes, the controller must be retuned by approximately the relative gain, (Kc)dec   (Kc)SL .
When a valve saturates, the “other” loops need to be retuned again!
The behavior with integral windup is complex.
Why not use MPC?

## Slide 36
MULTILOOP CONTROL PERFORMANCE
CONCLUSIONS
CONTROL PERFORMANCE DEPENDS STRONGLY ON THE DISTURBANCE
- Multiloop systems have directions that are easy/difficult to achieve
- Multiloop performance can be worse or better than SL
SHORT-CUT METHOD IS AVAILABLE TO EVALUATE MULTILOOP PERFORMANCE
- RDG uses steady-state gains
- Large value is BAD; small value might be good
(careful of +/- cancellation)

## Slide 37
MULTILOOP CONTROL PERFORMANCE
Complete the following table with recommendations for control design