## Slide 1
Process Operability Class Materials
Operating Window
Copyright © Thomas Marlin 2019
The copyright holder provides a royalty-free license for use of this material at non-profit educational institutions
FC
1
LC
1
Basic flowsheet
Design with Operability

## Slide 2
Key Operability issues
1. Operating window
2. Flexibility/
controllability
3. Reliability
4. Safety & equipment protection
5. Efficiency & profitability
6. Operation during transitions
7. Dynamic Performance
8. Monitoring & diagnosis
Figure citation 1 Rebecca Clements (2019)
My cell phone only works when I’m within 1 km of a cell tower
My cell phone only works when the temperature is 15-25 °C!
Chapter 2 Operating Window
Essentially every device we own has a limited operating window. How do you define an acceptable window?
This operating window is too small; it limits the application of the device!

## Slide 3
feasible
Key Operability issues
1. Operating window
2. Flexibility/
controllability
3. Reliability
4. Safety & equipment protection
5. Efficiency & profitability
6. Operation during transitions
7. Dynamic Performance
8. Monitoring & diagnosis
Chapter 2 Operating Window
Every process that we design and operate has an operating window that strongly effects the capital and operating costs.
We better learn how to design the best
operating window!

## Slide 4
Key Operability issues
1. Operating window
2. Flexibility/
controllability
3. Reliability
4. Safety & equipment protection
5. Efficiency & profitability
6. Operation during transitions
7. Dynamic Performance
8. Monitoring & diagnosis
Chapter 2 Operating Window
Lesson Outline
Operability Window Problem Definition
- Variability
- Bounds
- Integrity Operating Window (IOW)
- Turndown
- Selecting capacity
Operating Window Calculations
Let’s start here

## Slide 5
Key Operability issues
1. Operating window
2. Flexibility/
controllability
3. Reliability
4. Safety & equipment protection
5. Efficiency & profitability
6. Operation during transitions
7. Dynamic Performance
8. Monitoring & diagnosis
Chapter 2 Operating Window
An operating window defines the achievable operation of a flexible process when considering the expected range of variability and the bounds on equipment performance.
Variability - We consider the range of variability that is likely to occur and for which the process should remain in operation. (For very large variability, the process may shutdown or be expected to produce unacceptable products.)
How can the process function successfully, meeting all performance requirements when variability occurs?

## Slide 6
Key Operability issues
1. Operating window
2. Flexibility/
controllability
3. Reliability
4. Safety & equipment protection
5. Efficiency & profitability
6. Operation during transitions
7. Dynamic Performance
8. Monitoring & diagnosis
Chapter 2 Operating Window
An operating window defines the achievable operation
Variability - We consider the range of variability that is likely to occur.
Bounds – All equipment have upper and lower limits on the variables defining its operation.
Capacity – The equipment should be designed to have sufficient capacity to achieve desired performance for the defined variability.
Flexibility – The equipment design must be enhanced to allow its performance to be modified in response to variability
Next chapter

## Slide 7
Key Operability issues
1. Operating window
2. Flexibility/
controllability
3. Reliability
4. Safety & equipment protection
5. Efficiency & profitability
6. Operation during transitions
7. Dynamic Performance
8. Monitoring & diagnosis
Chapter 2 Operating Window
Sources of variability were introduced in Chapter 1.
Deliberate changes
Disturbances
Mismatch from design models
Equipment performance
Human error
Can you find one example of each in this flash process?

## Slide 8
FR
FV
xB
xD
Key Operability issues
1. Operating window
2. Flexibility/
controllability
3. Reliability
4. Safety & equipment protection
5. Efficiency & profitability
6. Operation during transitions
7. Dynamic Performance
8. Monitoring & diagnosis
Sources of variability
Deliberate changes
Disturbances
Mismatch from design models
Equipment performance
Human error
Chapter 2 Operating Window
Class workshop – Identify at least one source of variability from each category for a distillation tower.

## Slide 9
FR
FV
xB
xD
Key Operability issues
1. Operating window
2. Flexibility/
controllability
3. Reliability
4. Safety & equipment protection
5. Efficiency & profitability
6. Operation during transitions
7. Dynamic Performance
8. Monitoring & diagnosis
Sources of variability
Deliberate changes
Disturbances
Mismatch from design models
Equipment performance
Human error
Chapter 2 Operating Window
Class workshop – Identify at least one source of variability from each category for a distillation tower.
Deliberate: feed flow rate
Disturbance:
feed composition
Model mismatch: Vapor-liquid equilibrium,
Tray efficiencies
Equipment performance: Reboiler fouling
Human error: important for safety analysis, not for (normal) operating window

## Slide 10
Heat exchanger Q = U AY (T)lm
Class workshop
What is the “worst case” variability (operating conditions) we would use to design the heat exchanger?
What design parameter(s) are selected for the worst case?
Hot process fluid into shell
Cooling water into tubes
Key Operability issues
1. Operating window
2. Flexibility/
controllability
3. Reliability
4. Safety & equipment protection
5. Efficiency & profitability
6. Operation during transitions
7. Dynamic Performance
8. Monitoring & diagnosis
The goal is to cool this stream
Chapter 2 Operating Window

## Slide 11
Solution
1. The design specification will define a boundary of the operating window – The Worst Case gives the largest area for heat exchange.
Hot process fluid into shell
Cooling water into tubes
Highest flow rate,
Highest temperature
Lowest temperature
Lowest flow rate,
Highest temperature
Greatest fouling,
Lowest U
Key Operability issues
1. Operating window
2. Flexibility/
controllability
3. Reliability
4. Safety & equipment protection
5. Efficiency & profitability
6. Operation during transitions
7. Dynamic Performance
8. Monitoring & diagnosis
Chapter 2 Operating Window

## Slide 12
Solution
2. Design parameter is area.
Key Operability issues
1. Operating window
2. Flexibility/
controllability
3. Reliability
4. Safety & equipment protection
5. Efficiency & profitability
6. Operation during transitions
7. Dynamic Performance
8. Monitoring & diagnosis
Chapter 2 Operating Window
Heat exchanger Q= FρCp(Tin-Tout) = U AY (T)lm
A = {FρCp(Tin-Tout)}/{UY(T)lm}

## Slide 13
Class Workshop: Determine typical bounds (limitations, constraints) that affect the operating window for a distillation tower.
FR
FV
xB
xD
Key Operability issues
1. Operating window
2. Flexibility/
controllability
3. Reliability
4. Safety & equipment protection
5. Efficiency & profitability
6. Operation during transitions
7. Dynamic Performance
8. Monitoring & diagnosis
Chapter 2 Operating Window

## Slide 14
Class Workshop: Solution for Distillation Constraints
FR
FV
xB
xD
Pumping, pipe, valve capacity
Maximum cooling capacity
Maximum and minimum liquid and vapor flow rates
Maximum and minimum liquid and vapor flow rates
Flow pipe, valve capacity
Maximum heating
Minimum natural circulation to reboiler
Product composition
Product composition
Key Operability issues
1. Operating window
2. Flexibility/
controllability
3. Reliability
4. Safety & equipment protection
5. Efficiency & profitability
6. Operation during transitions
7. Dynamic Performance
8. Monitoring & diagnosis
Chapter 2 Operating Window

## Slide 15
Class Workshop: The operating window for the internal flowa in a trayed column
Key Operability issues
1. Operating window
2. Flexibility/
controllability
3. Reliability
4. Safety & equipment protection
5. Efficiency & profitability
6. Operation during transitions
7. Dynamic Performance
8. Monitoring & diagnosis
Chapter 2 Operating Window
During design, the window size can be changed through selection of tray type (bubble cap, sieve, valve, etc.)
During operation, internal flows determined by feed, reflux, and reboil
Citation 3
Citation 4

## Slide 16
Class Workshop: Bound on the reboiler temperature difference to prevent film boiling.
Key Operability issues
1. Operating window
2. Flexibility/
controllability
3. Reliability
4. Safety & equipment protection
5. Efficiency & profitability
6. Operation during transitions
7. Dynamic Performance
8. Monitoring & diagnosis
Chapter 2 Operating Window
Nucleate boiling - OK
Film boiling –Not OK

## Slide 17
Key Operability issues
1. Operating window
2. Flexibility/
controllability
3. Reliability
4. Safety & equipment protection
5. Efficiency & profitability
6. Operation during transitions
7. Dynamic Performance
8. Monitoring & diagnosis
Chapter 2 Operating Window
Lesson Outline
Operability Window Problem Definition
- Variability
- Bounds
- Integrity Operating Window (IOW)
- Turndown
- Selecting capacity
Operating Window Calculations

## Slide 18
Chapter 2 Operating Window
Selecting bounds based on the Integrity Operating Window
Ensures that the longer-term operation of the equipment is not sacrificed for short-term gains
Critical limit high Failure occurs quickly
Critical limit low Failure occurs quickly
Standard level high Failure occurs with sustained operation
Standard level low Failure occurs with sustained operation
Safe operation
Target range high
Target range low
Stable, reliable
Target (optimal)

## Slide 19
Chapter 2 Operating Window
Class Workshop – For the reforming process, identify bounds
That are “hard’, i.e., cannot be violated
That are “soft”, i.e., can be violated but violation degrades equipment
Citation 2

## Slide 20
Chapter 2 Operating Window
Class Workshop – For the reforming process, identify bounds
That are “hard’, i.e., cannot be violated
That are “soft”, i.e., can be violated but violation degrades equipment
Minimum flow rate through compressor
Minimum excess air to burners in each fired heater
Minimum and maximum liquid and vapor flows on each tray
Citation ?

## Slide 21
Chapter 2 Operating Window
Class Workshop – For the reforming process, identify bounds
That are “hard’, i.e., cannot be violated
That are “soft”, i.e., can be violated but violation degrades equipment
Flow far from best efficiency point
Maximum tube metal temperature
Maximum catalyst temperature

## Slide 22
Key Operability issues
1. Operating window
2. Flexibility/
controllability
3. Reliability
4. Safety & equipment protection
5. Efficiency & profitability
6. Operation during transitions
7. Dynamic Performance
8. Monitoring & diagnosis
Chapter 2 Operating Window
High and Low Bounds Exist for Most Equipment
Turndown ratio
is the normal maximum value of a variable divided by the normal minimum valve of the variable. The modifier “normal” is included to limit the range of the variable to values that can be sustained reliably over a long time without hazard or damage to equipment.

## Slide 23
Engineer must define the variability (set points and disturbances) and identify key bounds in equipment.
Based on above information, the operating window and equipment capacity is determined.
Key Operability issues
1. Operating window
2. Flexibility/
controllability
3. Reliability
4. Safety & equipment protection
5. Efficiency & profitability
6. Operation during transitions
7. Dynamic Performance
8. Monitoring & diagnosis
Chapter 2 Operating Window
Variability
Bounds (Limits)
Operating window
Flexibility
Next chapter

## Slide 24
In general, we want a large operating window. Why not always design and construct equipment with very large capacities?
Class Workshop: Complete the following table.
Advantages
Disadvantages
Small equipment*
Large equipment
Key Operability issues
1. Operating window
2. Flexibility/
controllability
3. Reliability
4. Safety & equipment protection
5. Efficiency & profitability
6. Operation during transitions
7. Dynamic Performance
8. Monitoring & diagnosis
* = small equipment just satisfies single, base-case design point
Chapter 2 Operating Window

## Slide 25
Class Workshop: Complete the following table.
Advantages
Disadvantages
Small equipment*
Lower capital cost
Most efficient at base case
Achieve “precise” operation (smaller equipment to adjust for flexibility)
Cannot achieve higher capacity
Cannot compensate for large range of disturbances
Might not achieve fast transition (no overshoot in manipulated variable)
Key Operability issues
1. Operating window
2. Flexibility/
controllability
3. Reliability
4. Safety & equipment protection
5. Efficiency & profitability
6. Operation during transitions
7. Dynamic Performance
8. Monitoring & diagnosis
* = small equipment just satisfies single, base-case design point
Chapter 2 Operating Window

## Slide 26
Class Workshop: Complete the following table.
Advantages
Disadvantages
Large equipment
Higher capital cost
Likely lower efficiency at base case and lower production rates
Might not achieve “precise” operation at base case
Can achieve higher capacity
Can compensate for likely range of disturbances
Can achieve faster transition (allows overshoot in manipulated variable)
Key Operability issues
1. Operating window
2. Flexibility/
controllability
3. Reliability
4. Safety & equipment protection
5. Efficiency & profitability
6. Operation during transitions
7. Dynamic Performance
8. Monitoring & diagnosis
Chapter 2 Operating Window

## Slide 27
Key Operability issues
1. Operating window
2. Flexibility/
controllability
3. Reliability
4. Safety & equipment protection
5. Efficiency & profitability
6. Operation during transitions
7. Dynamic Performance
8. Monitoring & diagnosis
Chapter 2 Operating Window
How do we select a capacity that is “just right”?
1. The process operation must always be safe.
2. We seek to avoid damage to expensive equipment.
3. We must produce products that satisfy quality requirements.
4. Capacity must satisfy 1-3 above for base case and frequently-occurring variability.
5. We can accept lower production rate for infrequent/abnormal production conditions.
6. We will stop production for extreme deviations.

## Slide 28
Key Operability issues
1. Operating window
2. Flexibility/
controllability
3. Reliability
4. Safety & equipment protection
5. Efficiency & profitability
6. Operation during transitions
7. Dynamic Performance
8. Monitoring & diagnosis
Chapter 2 Operating Window
How do we select a capacity that is “just right”?
1. The process operation must always be safe.
2. We seek to avoid damage to expensive equipment.
3. We must produce products that satisfy quality requirements.
4. Capacity must satisfy 1-3 above for base case and frequently-occurring variability.
We design for the smallest capacity that satisfies 1-4 above.
Conclusion

## Slide 29
Key Operability issues
1. Operating window
2. Flexibility/
controllability
3. Reliability
4. Safety & equipment protection
5. Efficiency & profitability
6. Operation during transitions
7. Dynamic Performance
8. Monitoring & diagnosis
Chapter 2 Operating Window
We design for the smallest capacity that satisfies 1-4 above.
Variable 1
Variable 2
Equipment capacity too large
Variable 1
Variable 2
Equipment capacity too small
Variable 1
Variable 2
Equipment capacity OK

## Slide 30
Key Operability issues
1. Operating window
2. Flexibility/
controllability
3. Reliability
4. Safety & equipment protection
5. Efficiency & profitability
6. Operation during transitions
7. Dynamic Performance
8. Monitoring & diagnosis
Chapter 2 Operating Window
Lesson Outline
Operability Window Problem Definition
Operating Window Calculations
- Method
- Linear Example
- Non-linear Process Example
- Selecting Manipulated Variable
- Limitations

## Slide 31
Key Operability issues
1. Operating window
2. Flexibility/
controllability
3. Reliability
4. Safety & equipment protection
5. Efficiency & profitability
6. Operation during transitions
7. Dynamic Performance
8. Monitoring & diagnosis
Chapter 2 Operating Window
Calculating the Steady-state Operating Window
4. Report results and display graphically.
Iterate often to obtain a good estimate of the operating window size
A base case design is simulated using steady-state flowsheeting software.
Sample from the variable parameter distribution is taken to replace their base-case values, and the simulation is repeated.
3. Bounds on all variables are checked; if violation(s) exist, the point is marked as “infeasible. If no violations, mark “feasible”

## Slide 32
Key Operability issues
1. Operating window
2. Flexibility/
controllability
3. Reliability
4. Safety & equipment protection
5. Efficiency & profitability
6. Operation during transitions
7. Dynamic Performance
8. Monitoring & diagnosis
Chapter 2 Operating Window
Calculating the Steady-state Operating Window
Note: Distributions can (and usually do) have more complex shapes

## Slide 33
Key Operability issues
1. Operating window
2. Flexibility/
controllability
3. Reliability
4. Safety & equipment protection
5. Efficiency & profitability
6. Operation during transitions
7. Dynamic Performance
8. Monitoring & diagnosis
Chapter 2 Operating Window
Class Workshop: Calculate the operating window for a process described by the following linear model.
y = A *u + B *d + c
y = vector of dependent variables (i.e., controlled variables)
u = vector of adjustable independent variables (i.e., a manipulated variables)
d = vector of independent variables that cannot be directly adjusted (i.e., a disturbances)
A, B, c = parameters, vector or matrix as appropriate

## Slide 34
Key Operability issues
1. Operating window
2. Flexibility/
controllability
3. Reliability
4. Safety & equipment protection
5. Efficiency & profitability
6. Operation during transitions
7. Dynamic Performance
8. Monitoring & diagnosis
Chapter 2 Operating Window
y = A *u + B *d + c
Constant; no disturbances
Allowed to vary over anticipated range.
Calculated for each set of values for the manipulated variables.
Note: Arrows show order of calculation, which in this case is the same as causality in physical system.

## Slide 35
Key Operability issues
1. Operating window
2. Flexibility/
controllability
3. Reliability
4. Safety & equipment protection
5. Efficiency & profitability
6. Operation during transitions
7. Dynamic Performance
8. Monitoring & diagnosis
Chapter 2 Operating Window
y = A *u + B *d + c
Allowed to vary over range
Calculated for each set of values in the disturbance variability range .
Constant; must satisfy set points.
Note: Arrows show order of calculation, not causality in physical system.

## Slide 36
Key Operability issues
1. Operating window
2. Flexibility/
controllability
3. Reliability
4. Safety & equipment protection
5. Efficiency & profitability
6. Operation during transitions
7. Dynamic Performance
8. Monitoring & diagnosis
Chapter 2 Operating Window
Class Workshop – Determine the operating window for the two product distillation tower shown below. Specifically, determine the range of manipulated variables (FV and FR) required for disturbances in the feed flow rate and feed composition.
Feed rate
4-14 kmole/min
Feed L.K.
0.30-0.60 mole fraction

## Slide 37
Key Operability issues
1. Operating window
2. Flexibility/
controllability
3. Reliability
4. Safety & equipment protection
5. Efficiency & profitability
6. Operation during transitions
7. Dynamic Performance
8. Monitoring & diagnosis
Chapter 2 Operating Window

## Slide 38
Key Operability issues
1. Operating window
2. Flexibility/
controllability
3. Reliability
4. Safety & equipment protection
5. Efficiency & profitability
6. Operation during transitions
7. Dynamic Performance
8. Monitoring & diagnosis
Chapter 2 Operating Window
Lesson Outline
Operability Window Problem Definition
Operating Window Calculations
- Method
- Linear Example
- Non-linear Process Example
- Selecting Manipulated Variable
- Limitations

## Slide 39
Key Operability issues
1. Operating window
2. Flexibility/
controllability
3. Reliability
4. Safety & equipment protection
5. Efficiency & profitability
6. Operation during transitions
7. Dynamic Performance
8. Monitoring & diagnosis
Chapter 2 Operating Window
How do we properly select manipulated variables?
Key aspects of manipulated variable selection
1. Each has a strong effect on controlled output variable
ui * Ki = yi
Ki should be “large” to provide correction for disturbances to one or more yi

## Slide 40
Key Operability issues
1. Operating window
2. Flexibility/
controllability
3. Reliability
4. Safety & equipment protection
5. Efficiency & profitability
6. Operation during transitions
7. Dynamic Performance
8. Monitoring & diagnosis
Chapter 2 Operating Window
How do we properly select manipulated variables?
Key aspects of manipulated variable selection
1. Each has a strong effect on controlled output variable
2. Controllable system – Affect all controlled variables independently using all manipulated variables.
y = A *u + B *d + c
y = vector of dependent variables (i.e., controlled variables)
u = vector of adjustable independent variables (i.e., a manipulated variables)
d = vector of independent variables that cannot be directly adjusted (i.e., a disturbances)
A, B, c = parameters, vector or matrix as appropriate
u = A-1 [ y + B *d + c]
Det (A) ≠ 0

## Slide 41
Key Operability issues
1. Operating window
2. Flexibility/
controllability
3. Reliability
4. Safety & equipment protection
5. Efficiency & profitability
6. Operation during transitions
7. Dynamic Performance
8. Monitoring & diagnosis
Chapter 2 Operating Window
How do we properly select manipulated variables?
Key aspects of manipulated variable selection
1. Each has a strong effect on controlled output variable
2. Controllable system – Affect all controlled variables independently using all manipulated variables.
3. Range – Able to achieve all desired controlled variable values with disturbances occurring.
Controlled variables
Disturbance variables
Manipulated variables
Process design must be able to achieve this range of adjustments

## Slide 42
Key Operability issues
1. Operating window
2. Flexibility/
controllability
3. Reliability
4. Safety & equipment protection
5. Efficiency & profitability
6. Operation during transitions
7. Dynamic Performance
8. Monitoring & diagnosis
Chapter 2 Operating Window
How do we properly select manipulated variables?
Key aspects of manipulated variable selection
1. Each has a strong effect on controlled output variable
2. Controllable system – Affect all controlled variables independently using all manipulated variables.
3. Range – Able to achieve all desired controlled variable values with disturbances occurring.
5. Dynamics – Fast feedback dynamics able to respond quickly to disturbances.
4. Independence – Adjustments should not cause disturbances or high cost to remainder of process.

## Slide 43
Key Operability issues
1. Operating window
2. Flexibility/
controllability
3. Reliability
4. Safety & equipment protection
5. Efficiency & profitability
6. Operation during transitions
7. Dynamic Performance
8. Monitoring & diagnosis
Chapter 2 Operating Window
Limitations to this Operating Window Analysis
1. Only steady-state behavior is considered. Transient operation can have a larger range.
2. Large excursions, (e.g., startup and shutdown, major faults, etc.) are not considered.
3. It is assumed that the process has only one steady-state operating point for each case.
4. Model structural uncertainty not addressed.
5. “Curse of dimensionality” when numerous variables are included in the variability cases.

## Slide 44
Typical Industrial Practice
SAFETY FACTORS: Some “safety factor” is built into the design procedure. After we have calculated the required pipe diameter, valve diameter, vessel size, motor power etc., we purchase the closest available size.
Since the manufactured sizes are discrete, we select the next largest size.
This provides some safety margin.
Key Operability issues
1. Operating window
2. Flexibility/
controllability
3. Reliability
4. Safety & equipment protection
5. Efficiency & profitability
6. Operation during transients
7. Dynamic Performance
8. Monitoring & diagnosis
Chapter 2 Operating Window

## Slide 45
This is not engineering! Any single factor would be too small for some equipment and too large for others.
After applying the proper operating window analysis, a small safety factor can be employed for modelling uncertainty, based on experience. Typical values are 10-15%.
“For well tested process, safety factors can approach 0%” *
* Valle-Riestra, J.F. (Dow Chemical Co.), Project Evaluation in the Process Industries, McGraw-Hill, New York, 1983 (pg 209)
Key Operability issues
1. Operating window
2. Flexibility/
controllability
3. Reliability
4. Safety & equipment protection
5. Efficiency & profitability
6. Operation during transients
7. Dynamic Performance
8. Monitoring & diagnosis
Chapter 2 Operating Window
SAFETY FACTORS: Couldn’t we just design for the base case and multiply every capacity by a safety factor,
(1+ X/100) with X = 25%, 35%, 50%, ….
Typical Industrial Practice

## Slide 46
Design Procedure
Set goals and design specifications
Select process technology
Define process structure (sequence)
Simulate the flowsheet
Design equipment
The flowsheet typically involves basic M&E balances, equilibrium and rate processes. It does not consider practical issues for achieving the operation.
Equipment design achieves the base case flowsheet (plus other concerns). This sets the “capacity” of the plant.
The design must define the range of operations (set points and disturbances) to be achieved.
We can accept less than full production rate or top efficiency for extreme situations.
We must document specifications and range or operations and review with all stakeholders!
These “specifications” are in the
Design Basis Memorandum.
Chapter 2 Operating Window
Important variability should be defined as an integral part of the project definition.

## Slide 47
Key Operability issues
1. Operating window
2. Flexibility/
controllability
3. Reliability
4. Safety & equipment protection
5. Efficiency & profitability
6. Operation during transitions
7. Dynamic Performance
8. Monitoring & diagnosis
Chapter 2 Operating Window
Conclusions
The operating window analysis determines the capacity of process equipment and the range over which it operates.
How can we change the operation of equipment, e.g.,
“ How can we change the duty of a heat exchanger after is has been built and installed?”
Then, we address subsequent issues;
Reliability
Safety
Control
…………………

## Slide 48
1. Rebecca Clements (2019) Dopamine, Smartphones and You, SITNBoston is licensed under a Creative Commons Attribution-NonCommercial-ShareAlike 4.0 International License. http://sitn.hms.harvard.edu/flash/2018/dopamine-smartphones-battle-time/
Key Operability issues
1. Operating window
2. Flexibility/
controllability
3. Reliability
4. Safety & equipment protection
5. Efficiency & profitability
6. Operation during transients
7. Dynamic Performance
8. Monitoring & diagnosis
Chapter 2 Operating Window
Citations
2. Mbeychok, Milton https://commons.wikimedia.org/wiki/File:CatReformer.png
3. Padleckis, H., (2006A) (visited 2019)
https://commons.wikimedia.org/wiki/File:Bubble_Cap_Trays.PNG
4. Pickerton et. al. (2014) visited 2019, Northwestern University https://processdesign.mccormick.northwestern.edu/index.php/Separation_processes

## Slide 49
WORKSHOPS
Flip the Classroom: Since you have engaged the basic material in the eLearning format, you are prepared to perform these workshops as class exercises.
You have complained that lectures are boring; now, you get to be active by solving problems during class !
To improve the learning experience, we recommend that you perform these exercises in small groups.
Please be sure to record your questions and bring them to the attention of your instructor.
Key Operability issues
1. Operating window
2. Flexibility/
controllability
3. Reliability
4. Safety & equipment protection
5. Efficiency & profitability
6. Operation during transients
7. Dynamic Performance
8. Monitoring & diagnosis
Chapter 2 Operating Window

## Slide 50
Consider the flow system. What variables must we determine? What is the “worst case” we would use to design the system, specifically the required pump outlet pressure?
Key Operability issues
1. Operating window
2. Flexibility/
controllability
3. Reliability
4. Safety & equipment protection
5. Efficiency & profitability
6. Operation during transitions
7. Dynamic Performance
8. Monitoring & diagnosis
Chapter 2 Operating Window
Workshop 1

## Slide 51
Solution - The design will define a boundary of the operating window - Worst case gives the largest pump.
What variables must we determine?
- Pipe diameter - by guideline liquid velocity ≈ 1 m/s ( Gas: 30 m/s)
- Pump horsepower - from highest flow rate and PP and
the lowest suction pressure
Pp
Highest vessel
pressure
Highest
pressure drop
Highest
pressure drop
Highest flow,
largest friction
factor
Lowest level
(lowest head)
Key Operability issues
1. Operating window
2. Flexibility/
controllability
3. Reliability
4. Safety & equipment protection
5. Efficiency & profitability
6. Operation during transitions
7. Dynamic Performance
8. Monitoring & diagnosis
Chapter 2 Operating Window

## Slide 52
Key Operability issues
1. Operating window
2. Flexibility/
controllability
3. Reliability
4. Safety & equipment protection
5. Efficiency & profitability
6. Operation during transitions
7. Dynamic Performance
8. Monitoring & diagnosis
Chapter 2 Operating Window
Equipment must function correctly within the operating window. Discuss issues that would limit the usefulness of the flow sensor measurement and suggest improvements to the design.
heating
FC
Cold (20C) liquid
Orifice meter
Workshop 2

## Slide 53
Porifice=P1 – P3
Distance 
pressure
Porifice
Measure pressure drop
Key Operability issues
1. Operating window
2. Flexibility/
controllability
3. Reliability
4. Safety & equipment protection
5. Efficiency & profitability
6. Operation during transitions
7. Dynamic Performance
8. Monitoring & diagnosis
Chapter 2 Operating Window

## Slide 54
Bernoulli’s eqn.
General meter eqn.
Installed orifice meter
(requires density measurement)
0 = aver. density
C0 = constant for specific meter
Installed orifice meter
(assuming constant density)
Most common flow calculation, does not require density measurement
v = velocity
F = volumetric flow rate
f = frictional losses
= density
A = cross sectional area
Relate the pressure drop to the flow rate

## Slide 55
P
cooling

K
Take square root of measurement
Multiply signal by meter constant K
FC
Measure pressure difference
“Measured value” to flow controller
When an orifice meter is used, the calculations in yellow are performed. Typically, they are not shown on a process drawing.
liquid

## Slide 56
General meter eqn.
v = velocity
F = volumetric flow rate
f = frictional losses
= density
A = cross sectional area
Relate the pressure drop to the flow rate
Cmeter
Reynolds number
We assume that the meter coefficient is constant. The flow accuracy is acceptable only for higher values of flow, typically 25-100% of the maximum for an orifice

## Slide 57
Porifice=P1 – P3
Distance 
pressure
What is a key disadvantage of the orifice meter?
Pressure loss!
When cost of pressure increase (P1) by pumping or compression is high, we want to avoid the “non-recoverable” pressure loss.
Ploss = P1 – P2
Non-recoverable pressure drop

## Slide 58
Equipment must function correctly within the operating window
heating
FC
Velocity increases; Bernoulli says that pressure decreases
The fluid can partially vaporize.
The pressure difference will
not reliability indicate
the flow rate!
Cold (20C) liquid
Orifice meter
Key Operability issues
1. Operating window
2. Flexibility/
controllability
3. Reliability
4. Safety & equipment protection
5. Efficiency & profitability
6. Operation during transitions
7. Dynamic Performance
8. Monitoring & diagnosis
Chapter 2 Operating Window

## Slide 59
Equipment must function correctly within the operating window
heating
Simple solution,
Locate flow
measurement where the
pressure is highest
and temperature lowest.
Ensure that flashing does not
occur - design calc’s
FC
Cold (20C) liquid
Key Operability issues
1. Operating window
2. Flexibility/
controllability
3. Reliability
4. Safety & equipment protection
5. Efficiency & profitability
6. Operation during transitions
7. Dynamic Performance
8. Monitoring & diagnosis
Chapter 2 Operating Window

## Slide 60
Key Operability issues
1. Operating window
2. Flexibility/
controllability
3. Reliability
4. Safety & equipment protection
5. Efficiency & profitability
6. Operation during transitions
7. Dynamic Performance
8. Monitoring & diagnosis
Chapter 2 Operating Window
Workshop 3
Equipment must function correctly within the operating window. Discuss the meaning of cavitation and how it can influence the design of the inventory and pumping at the bottoms of a distillation column.
Bottoms product
reboiler
Centrifugal pump

## Slide 61
Key Operability issues
1. Operating window
2. Flexibility/
controllability
3. Reliability
4. Safety & equipment protection
5. Efficiency & profitability
6. Operation during transitions
7. Dynamic Performance
8. Monitoring & diagnosis
Chapter 2 Operating Window
Workshop 3
Bottoms product
reboiler
Centrifugal pump
Pressure drop due to flow frictional losses
Pressure drop due to the velocity increase in the eye of the pump
What happens
in the
pump?

## Slide 62
Equipment must function correctly within the operating window
Bottoms product
reboiler
Centrifugal pump
Cavitation: The liquid partially vaporizes. As the pressure increases in the pump, the vapor is subsequently condensed. This collapsing of bubbles (cavitation ) causes noise, vibration and erosion - all of which are bad.
Key Operability issues
1. Operating window
2. Flexibility/
controllability
3. Reliability
4. Safety & equipment protection
5. Efficiency & profitability
6. Operation during transitions
7. Dynamic Performance
8. Monitoring & diagnosis
Chapter 2 Operating Window

## Slide 63
Equipment must function correctly within the operating window
Bottoms product
reboiler
Centrifugal pump
This liquid head increases the pressure at the inlet to the pump and prevents cavitation.
NPSHR: The manufacturer must define the minimum net positive suction head required.
The process engineer must design to provide it. NPSHA>NPSHR
Key Operability issues
1. Operating window
2. Flexibility/
controllability
3. Reliability
4. Safety & equipment protection
5. Efficiency & profitability
6. Operation during transitions
7. Dynamic Performance
8. Monitoring & diagnosis
NPSHA
Chapter 2 Operating Window

## Slide 64
Equipment must function correctly within the operating window
NPSHR: The manufacturer must define the minimum net positive suction head required.
From: Woods, D.R., Process Design and Engineering Practice, Prentice -Hall, 1995
The process engineer must design to provide it. How?
This is issue when liquid is at (near) its bubble point. Give examples when this is the situation in chemical processes.
Elevate the liquid above the pump (two ways)
Reduce friction losses
Subcool the liquid (careful of added pressure drop)
Key Operability issues
1. Operating window
2. Flexibility/
controllability
3. Reliability
4. Safety & equipment protection
5. Efficiency & profitability
6. Operation during transitions
7. Dynamic Performance
8. Monitoring & diagnosis
Chapter 2 Operating Window

## Slide 65
Equipment must function correctly within the operating window
From: Woods, D.R., Process Design and Engineering Practice, Prentice -Hall, 1995
This is issue when liquid is at (near) its bubble point. Give examples when this is the situation in chemical processes.
We deal with liquids at their bubble points often, for example,
Distillation/stripper bottoms
Distillation/absorber condensers and
OH drums
Flash drums
Concentration by boiling
Vapor compression refrigeration
Reactor cooling by solvent vaporization
Key Operability issues
1. Operating window
2. Flexibility/
controllability
3. Reliability
4. Safety & equipment protection
5. Efficiency & profitability
6. Operation during transitions
7. Dynamic Performance
8. Monitoring & diagnosis
Chapter 2 Operating Window

## Slide 66
Chapter 2 Operating Window
Workshop 4
Output controlled variables
Design
Process
Manipulated variables
Disturbances
Design values of the
disturbances
Each point is a sample from the possible adjustment range
Design
Complete the figure below with the general form of the Controlled variable region for as many cases as you can think of, including acceptable and unacceptable controllability.

## Slide 67
Chapter 2 Operating Window
Workshop 4
Complete the figure below with the general form of the Controlled variable region for as many cases as you can think of, including acceptable and unacceptable controllability.
Controllable
Uncontrollable
Large region
Small region
Ill-conditioned
Only CV1 affected
Only CV2 affected
Both affected, but not independently

## Slide 68
A  B
-rA = k0 e -E/RT CA
T
A
Reactant
Solvent
Coolant
Key Operability issues
1. Operating window
2. Flexibility/
controllability
3. Reliability
4. Safety & equipment protection
5. Efficiency & profitability
6. Operation during transitions
7. Dynamic Performance
8. Monitoring & diagnosis
Chapter 2 Operating Window
Workshop 5
Reactant concentration in reactor
Describe the shape of the operating window for the CSTR below and explain why it is not similar to a rectangle.

## Slide 69
Process without control
Manipulated variables
Disturbances
Output variables that we will wish to control
expected
High temperatures and high concentrations not possible because high temperatures cause fast reaction rate.
Low temperatures and low concentrations not possible because low temperatures cause slow reaction rate.
Workshop 5

## Slide 70
Read the following paper and discuss the following issues.
What is the relationship between “capacity” and “turndown”
Evaluate the definition of capacity in the paper; suggest additional issues needed.
Apply the results from part (2) to develop a definition of turndown.
Ogle, R. and A. Carpenter (2014) Calculating the Capacity of Chemical Plants, Chemical Engineering Progress, 110, No. 8, 59-63.
Key Operability issues
1. Operating window
2. Flexibility/
controllability
3. Reliability
4. Safety & equipment protection
5. Efficiency & profitability
6. Operation during transitions
7. Dynamic Performance
8. Monitoring & diagnosis
Chapter 2 Operating Window
Workshop 6