## Slide 1
Process Operability Class Materials
Process Flexibility
Copyright © Thomas Marlin 2019
The copyright holder provides a royalty-free license for use of this material at non-profit educational institutions
FC
1
LC
1
Basic flowsheet
Design with Operability

## Slide 2
Key Operability issues
1. Operating window
2. Flexibility/
controllability
3. Reliability
4. Safety & equipment protection
5. Efficiency & profitability
6. Operation during transitions
7. Dynamic Performance
8. Monitoring & diagnosis
Chapter 3 Flexibility
When you design an automobile, your customers would appreciate a way to steer the vehicle! Seems pretty obvious, but have you thought about the way to control all of the equipment that you have learned about: flow, heat transfer mass transfer, chemical reactor, etc.
One important aspect of the design is the addition of flexibility – ways to adjust the operation
This diagram shows rack and pinion steering. The engineers had to include this in the design.
What about your process design?
Citation 6

## Slide 3
Key Operability issues
1. Operating window
2. Flexibility/
controllability
3. Reliability
4. Safety & equipment protection
5. Efficiency & profitability
6. Operation during transitions
7. Dynamic Performance
8. Monitoring & diagnosis
Chapter 3 Flexibility
Where do we stand after completing the previous chapter on the Operating Window?
We have selected candidate controlled variables and candidate adjusted variables based on steady-state behavior – it provides the range of effects required.
In the heat exchanger network, the operating window requires the heat transfer to be adjusted.
What adjustable equipment can be installed to affect the heat duty (remember, the heat exchanger has been installed)?
How can the adjustments be automated?
subsequent chapters
this chapter

## Slide 4
Key Operability issues
1. Operating window
2. Flexibility/
controllability
3. Reliability
4. Safety & equipment protection
5. Efficiency & profitability
6. Operation during transitions
7. Dynamic Performance
8. Monitoring & diagnosis
Chapter 3 Flexibility
Lesson Outline
Flexibility for Fluid Flow
Flexibility for Heat Transfer
Production Control
Unit Operation
- Boiler and Steam System

## Slide 5
Key Operability issues
1. Operating window
2. Flexibility/
controllability
3. Reliability
4. Safety & equipment protection
5. Efficiency & profitability
6. Operation during transitions
7. Dynamic Performance
8. Monitoring & diagnosis
Chapter 3 Flexibility
To state the obvious, we have to move material around in the process. Since Chemical Engineering deals mostly with fluids, we will concentrate on
Flexibility For Fluid Flow
What affects the flowrate?
What can be adjusted?

## Slide 6
Key Operability issues
1. Operating window
2. Flexibility/
controllability
3. Reliability
4. Safety & equipment protection
5. Efficiency & profitability
6. Operation during transitions
7. Dynamic Performance
8. Monitoring & diagnosis
Chapter 3 Flexibility
Flexibility For Fluid Flow
Each term depends on the flow rate
Liquids

## Slide 7
Key Operability issues
1. Operating window
2. Flexibility/
controllability
3. Reliability
4. Safety & equipment protection
5. Efficiency & profitability
6. Operation during transitions
7. Dynamic Performance
8. Monitoring & diagnosis
Chapter 3 Flexibility
Flexibility For Fluid Flow
j = summation over all elements except the valve
The flow is influenced by the adjustable valve opening
∆Ppipe = pressure drop due to flow through pipe = f (L/D) ρF2/2g
∆Pi = pressure drop for all other elements = Ki ρF2/2g
Liquids

## Slide 8
Key Operability issues
1. Operating window
2. Flexibility/
controllability
3. Reliability
4. Safety & equipment protection
5. Efficiency & profitability
6. Operation during transitions
7. Dynamic Performance
8. Monitoring & diagnosis
Chapter 3 Flexibility
Flexibility For Fluid Flow
We cannot build our plants on a hillside, so we need pumps.
Centrifugal pump
Liquids

## Slide 9
Key Operability issues
1. Operating window
2. Flexibility/
controllability
3. Reliability
4. Safety & equipment protection
5. Efficiency & profitability
6. Operation during transitions
7. Dynamic Performance
8. Monitoring & diagnosis
Chapter 3 Flexibility
Flexibility For Fluid Flow
Typical pump performance curve
Liquids
Citation 1

## Slide 10
Key Operability issues
1. Operating window
2. Flexibility/
controllability
3. Reliability
4. Safety & equipment protection
5. Efficiency & profitability
6. Operation during transitions
7. Dynamic Performance
8. Monitoring & diagnosis
Chapter 3 Flexibility
Flow rate
Head at outlet of pump
To achieve the desired flow, we vary the system resistance by changing the valve opening that affects the valve pressure drop.
80%
60%
P2
M
Constant speed electric motor
Percent valve opening
100%
Flow rate with the valve 100% open.
Pump head
System losses
Flow flexibility through valve adjustments
Centrifugal pump
Liquids

## Slide 11
Key Operability issues
1. Operating window
2. Flexibility/
controllability
3. Reliability
4. Safety & equipment protection
5. Efficiency & profitability
6. Operation during transitions
7. Dynamic Performance
8. Monitoring & diagnosis
Chapter 3 Flexibility
Flow flexibility through speed adjustments
Centrifugal pump
Flow rate
Head at outlet of pump
To achieve the desired flow, we vary the the pump speed (rpm) with all valves fully opened.
P2
M
Pump head curves for different speeds with the same impeller diameter
Liquids

## Slide 12
Key Operability issues
1. Operating window
2. Flexibility/
controllability
3. Reliability
4. Safety & equipment protection
5. Efficiency & profitability
6. Operation during transitions
7. Dynamic Performance
8. Monitoring & diagnosis
Chapter 3 Flexibility
Liquids
Flexibility For Fluid Flow
Positive displacement pumps
Flexibility through speed adjustments, NOT valve adjustments
Positive displacement Gear pump
Citation 2

## Slide 13
Key Operability issues
1. Operating window
2. Flexibility/
controllability
3. Reliability
4. Safety & equipment protection
5. Efficiency & profitability
6. Operation during transitions
7. Dynamic Performance
8. Monitoring & diagnosis
Chapter 3 Flexibility
Flexibility For Fluid Flow
Gases
Compressor to increase gas pressure
How is flexibility introduced?
Centrifugal compressor
Citation 3

## Slide 14
Key Operability issues
1. Operating window
2. Flexibility/
controllability
3. Reliability
4. Safety & equipment protection
5. Efficiency & profitability
6. Operation during transitions
7. Dynamic Performance
8. Monitoring & diagnosis
Chapter 3 Flexibility
Flexibility For Fluid Flow
Gases
Compressor to increase gas pressure
Citation 5

## Slide 15
Key Operability issues
1. Operating window
2. Flexibility/
controllability
3. Reliability
4. Safety & equipment protection
5. Efficiency & profitability
6. Operation during transitions
7. Dynamic Performance
8. Monitoring & diagnosis
Chapter 3 Flexibility
Flexibility For Fluid Flow
Gases
Compressor to increase gas pressure
The compressor map shows that
The variables are the volumetric flow rate and pressure ratio
The speed affects the head
The maximum efficiency can be predicted
A minimum flow is needed to prevent surge
A maximum flow occurs at the stonewall

## Slide 16
Key Operability issues
1. Operating window
2. Flexibility/
controllability
3. Reliability
4. Safety & equipment protection
5. Efficiency & profitability
6. Operation during transitions
7. Dynamic Performance
8. Monitoring & diagnosis
Chapter 3 Flexibility
Flexibility For Fluid Flow
Gases
Compressor to increase gas pressure
Add flexibility

## Slide 17
Key Operability issues
1. Operating window
2. Flexibility/
controllability
3. Reliability
4. Safety & equipment protection
5. Efficiency & profitability
6. Operation during transitions
7. Dynamic Performance
8. Monitoring & diagnosis
Chapter 3 Flexibility
Lesson Outline
Flexibility for Fluid Flow
Flexibility for Heat Transfer
Production Control
Unit Operation
- Boiler and Steam System

## Slide 18
Key Operability issues
1. Operating window
2. Flexibility/
controllability
3. Reliability
4. Safety & equipment protection
5. Efficiency & profitability
6. Operation during transitions
7. Dynamic Performance
8. Monitoring & diagnosis
Chapter 3 Flexibility
Flexibility For Heat Transfer
Q = U A ∆T*
∆T* modified for equipment design, e.g., log-mean
Flexibility can be introduced by influencing any of the terms; U , A , or ∆T*.
Citation 4

## Slide 19
Key Operability issues
1. Operating window
2. Flexibility/
controllability
3. Reliability
4. Safety & equipment protection
5. Efficiency & profitability
6. Operation during transitions
7. Dynamic Performance
8. Monitoring & diagnosis
Chapter 3 Flexibility
Flexibility For Heat Transfer
Q = U A ∆T*
∆T* modified for equipment design, e.g., log-mean
Process stream
T
Utility stream
Flexibility through changing one total flow rate
Influences heat transfer coefficient
Utility adjustment does not influence production
Utility stream (cooling water, steam, etc.) must be provided in the plant design

## Slide 20
Key Operability issues
1. Operating window
2. Flexibility/
controllability
3. Reliability
4. Safety & equipment protection
5. Efficiency & profitability
6. Operation during transitions
7. Dynamic Performance
8. Monitoring & diagnosis
Chapter 3 Flexibility
Goal: Maintain cold effluent Tcold at a desired value
Stream A
(cold)
Stream B
(hot)
Freedom to adjust total flows
Stream A Stream B
1. Constant Adjustable
2. Adjustable Constant
3. Constant Constant
Class Workshop: Add flexibility to the heat exchanger to achieve the goal for three different scenarios. You may add piping and valve(s).
T
No phase change occurs to either stream.

## Slide 21
Key Operability issues
1. Operating window
2. Flexibility/
controllability
3. Reliability
4. Safety & equipment protection
5. Efficiency & profitability
6. Operation during transitions
7. Dynamic Performance
8. Monitoring & diagnosis
Chapter 3 Flexibility
Freedom to adjust total flow rates
Stream A Stream B
a. Constant Adjustable
b. Adjustable Constant
c. Constant Constant
Stream A
(cold)
Stream B
(hot)
TC
a
Stream A
(cold)
Stream B
(hot)
TC
c
Stream A
(cold)
Stream B
(hot)
TC
b
It is not typical to adjust a stream flow to control its temperature; if the temperature is important, likely the flow rate is also important.
Workshop solution

## Slide 22
Key Operability issues
1. Operating window
2. Flexibility/
controllability
3. Reliability
4. Safety & equipment protection
5. Efficiency & profitability
6. Operation during transitions
7. Dynamic Performance
8. Monitoring & diagnosis
Chapter 3 Flexibility
Stream A
(cold)
Stream B
(hot)
TC
Class Workshop: The previous solution for Case c is repeated below. The flexibility has a limited range of adjustment; complete by-pass is not possible. Improve the design to allow greater range from 0% to 100% by-pass flow.

## Slide 23
Key Operability issues
1. Operating window
2. Flexibility/
controllability
3. Reliability
4. Safety & equipment protection
5. Efficiency & profitability
6. Operation during transitions
7. Dynamic Performance
8. Monitoring & diagnosis
Chapter 3 Flexibility
Stream A
(cold)
Stream B
(hot)
TC
fc
fo
v100
v200
0 Controller output (%) 100
v100 percent open
0
0
100
100
v200 percent open
Workshop solution

## Slide 24
Key Operability issues
1. Operating window
2. Flexibility/
controllability
3. Reliability
4. Safety & equipment protection
5. Efficiency & profitability
6. Operation during transitions
7. Dynamic Performance
8. Monitoring & diagnosis
Chapter 3 Flexibility
Class Workshop: Liquid refrigerant is vaporizer while providing cooling in the heat exchanger shown below. Add flexibility so that the Stream A exit temperature can be controlled.
Helpful hint: The liquid level in the heat exchanger is stable.

## Slide 25
Key Operability issues
1. Operating window
2. Flexibility/
controllability
3. Reliability
4. Safety & equipment protection
5. Efficiency & profitability
6. Operation during transitions
7. Dynamic Performance
8. Monitoring & diagnosis
Chapter 3 Flexibility
Workshop solution: The rate of heat transfer depends on the area of the tubes that are in contact with the liquid refrigerant. Flexibility changes the liquid level.

## Slide 26
Key Operability issues
1. Operating window
2. Flexibility/
controllability
3. Reliability
4. Safety & equipment protection
5. Efficiency & profitability
6. Operation during transitions
7. Dynamic Performance
8. Monitoring & diagnosis
Chapter 3 Flexibility
Feed
Heat transfer medium
Effluent
Class Workshop: The stirred tank in the figure requires heating and cooling at different times. Add flexibility to provide the heat transfer.

## Slide 27
Key Operability issues
1. Operating window
2. Flexibility/
controllability
3. Reliability
4. Safety & equipment protection
5. Efficiency & profitability
6. Operation during transitions
7. Dynamic Performance
8. Monitoring & diagnosis
Chapter 3 Flexibility
Workshop solution: This design also includes a barrier between the heat and cooling fluids and the stirred tank.

## Slide 28
Key Operability issues
1. Operating window
2. Flexibility/
controllability
3. Reliability
4. Safety & equipment protection
5. Efficiency & profitability
6. Operation during transitions
7. Dynamic Performance
8. Monitoring & diagnosis
Chapter 3 Flexibility
Flexibility For Heat Transfer – Direct Mixing
Flexibility can be introduced using direct mixing.
The hydrocracker involves highly exothermic reactions.

## Slide 29
Key Operability issues
1. Operating window
2. Flexibility/
controllability
3. Reliability
4. Safety & equipment protection
5. Efficiency & profitability
6. Operation during transitions
7. Dynamic Performance
8. Monitoring & diagnosis
Chapter 3 Flexibility
Class Workshop: The design involves utilities for heating and cooling. Modify the design to retain flexibility and reduce utility costs.

## Slide 30
Key Operability issues
1. Operating window
2. Flexibility/
controllability
3. Reliability
4. Safety & equipment protection
5. Efficiency & profitability
6. Operation during transitions
7. Dynamic Performance
8. Monitoring & diagnosis
Chapter 3 Flexibility
Class Workshop: The design involves utilities for heating and cooling. Modify the design to retain flexibility and reduce utility costs.
Proposed solution 1: Discuss the strengths and weaknesses.

## Slide 31
Key Operability issues
1. Operating window
2. Flexibility/
controllability
3. Reliability
4. Safety & equipment protection
5. Efficiency & profitability
6. Operation during transitions
7. Dynamic Performance
8. Monitoring & diagnosis
Chapter 3 Flexibility
Class Workshop: The design involves utilities for heating and cooling. Modify the design to retain flexibility and reduce utility costs.
Proposed solution 2: Discuss the strengths and weaknesses.

## Slide 32
Key Operability issues
1. Operating window
2. Flexibility/
controllability
3. Reliability
4. Safety & equipment protection
5. Efficiency & profitability
6. Operation during transitions
7. Dynamic Performance
8. Monitoring & diagnosis
Chapter 3 Flexibility
Lesson Outline
Flexibility for Fluid Flow
Flexibility for Heat Transfer
Production Control
Unit Operation
- Boiler and Steam System

## Slide 33
Key Operability issues
1. Operating window
2. Flexibility/
controllability
3. Reliability
4. Safety & equipment protection
5. Efficiency & profitability
6. Operation during transitions
7. Dynamic Performance
8. Monitoring & diagnosis
Chapter 3 Flexibility
Flexibility For Production Control
Cannot match measured flows – measurement errors
One flexible variable sets production rate
Flows through the remainder of the process respond automatically, without human action

## Slide 34
Key Operability issues
1. Operating window
2. Flexibility/
controllability
3. Reliability
4. Safety & equipment protection
5. Efficiency & profitability
6. Operation during transitions
7. Dynamic Performance
8. Monitoring & diagnosis
Chapter 3 Flexibility
Flexibility For Production Control
Workshop: Ensure that (average) flows match throughout the process by controlling inventories, so that no material accumulation occurs.

## Slide 35
Key Operability issues
1. Operating window
2. Flexibility/
controllability
3. Reliability
4. Safety & equipment protection
5. Efficiency & profitability
6. Operation during transitions
7. Dynamic Performance
8. Monitoring & diagnosis
Chapter 3 Flexibility
Flexibility For Production Control
Solution: Level indicates liquid (solid) inventory, and pressure indicates vapor (or liquid-filled) inventory.

## Slide 36
Key Operability issues
1. Operating window
2. Flexibility/
controllability
3. Reliability
4. Safety & equipment protection
5. Efficiency & profitability
6. Operation during transitions
7. Dynamic Performance
8. Monitoring & diagnosis
Chapter 3 Flexibility
Flexibility For Production Control
Most production systems
Most utility systems

## Slide 37
Key Operability issues
1. Operating window
2. Flexibility/
controllability
3. Reliability
4. Safety & equipment protection
5. Efficiency & profitability
6. Operation during transitions
7. Dynamic Performance
8. Monitoring & diagnosis
Chapter 3 Flexibility
Flexibility For Production Control
Production rate controller
IC
= inventory controller
IC
IC
IC
IC
IC
IC
IC

## Slide 38
Chapter 3 Flexibility
Flexibility For Production Control

## Slide 39
Key Operability issues
1. Operating window
2. Flexibility/
controllability
3. Reliability
4. Safety & equipment protection
5. Efficiency & profitability
6. Operation during transitions
7. Dynamic Performance
8. Monitoring & diagnosis
Chapter 3 Flexibility
Lesson Outline
Flexibility for Fluid Flow
Flexibility for Heat Transfer
Production Control
Unit Operation
- Boiler and Steam System

## Slide 40
Key Operability issues
1. Operating window
2. Flexibility/
controllability
3. Reliability
4. Safety & equipment protection
5. Efficiency & profitability
6. Operation during transitions
7. Dynamic Performance
8. Monitoring & diagnosis
Chapter 3 Flexibility
Flexibility in Boiler and Steam System
Product system sets demands that must be satisfied by the steam system
Pull system!
Superheated steam for work; saturated steam for heat transfer
Heat transfer at several temperatures (pressures)
Entire supply system balanced automatically
All steam condensed and returned to boilers

## Slide 41
Key Operability issues
1. Operating window
2. Flexibility/
controllability
3. Reliability
4. Safety & equipment protection
5. Efficiency & profitability
6. Operation during transitions
7. Dynamic Performance
8. Monitoring & diagnosis
Chapter 3 Flexibility
Flexibility in Boiler and Steam System

## Slide 42
Key Operability issues
1. Operating window
2. Flexibility/
controllability
3. Reliability
4. Safety & equipment protection
5. Efficiency & profitability
6. Operation during transitions
7. Dynamic Performance
8. Monitoring & diagnosis
Chapter 3 Flexibility
Flexibility in Boiler and Steam System
High-pressure steam superheat flexibility
Direct mixing
Faster dynamics

## Slide 43
Key Operability issues
1. Operating window
2. Flexibility/
controllability
3. Reliability
4. Safety & equipment protection
5. Efficiency & profitability
6. Operation during transitions
7. Dynamic Performance
8. Monitoring & diagnosis
Chapter 3 Flexibility
Flexibility in Boiler and Steam System
Three-element Boiler Drum Level Control
Feedforward
Feedback
“Swell” occurs in riser and drum

## Slide 44
Key Operability issues
1. Operating window
2. Flexibility/
controllability
3. Reliability
4. Safety & equipment protection
5. Efficiency & profitability
6. Operation during transitions
7. Dynamic Performance
8. Monitoring & diagnosis
Chapter 3 Flexibility
Flexibility in Boiler and Steam System

## Slide 45
Key Operability issues
1. Operating window
2. Flexibility/
controllability
3. Reliability
4. Safety & equipment protection
5. Efficiency & profitability
6. Operation during transitions
7. Dynamic Performance
8. Monitoring & diagnosis
Chapter 3 Flexibility
Flexibility in Distillation
Flexibility for pressure control

## Slide 46
Key Operability issues
1. Operating window
2. Flexibility/
controllability
3. Reliability
4. Safety & equipment protection
5. Efficiency & profitability
6. Operation during transitions
7. Dynamic Performance
8. Monitoring & diagnosis
Chapter 3 Flexibility
Flexibility in Distillation
Flexibility for pressure control – Constant vapor product
CW
PC
LC

## Slide 47
Key Operability issues
1. Operating window
2. Flexibility/
controllability
3. Reliability
4. Safety & equipment protection
5. Efficiency & profitability
6. Operation during transitions
7. Dynamic Performance
8. Monitoring & diagnosis
Chapter 3 Flexibility
Flexibility in Distillation
Flexibility for pressure control – No vapor product

## Slide 48
Key Operability issues
1. Operating window
2. Flexibility/
controllability
3. Reliability
4. Safety & equipment protection
5. Efficiency & profitability
6. Operation during transitions
7. Dynamic Performance
8. Monitoring & diagnosis
Chapter 3 Flexibility
Flexibility in Distillation
Flexibility for pressure control – No vapor product
What can be adjusted?
Blade speed
Blade pitch
Louver position

## Slide 49
Key Operability issues
1. Operating window
2. Flexibility/
controllability
3. Reliability
4. Safety & equipment protection
5. Efficiency & profitability
6. Operation during transitions
7. Dynamic Performance
8. Monitoring & diagnosis
Chapter 3 Flexibility
Flexibility in Distillation
Flexibility for typical two-product tower

## Slide 50
Key Operability issues
1. Operating window
2. Flexibility/
controllability
3. Reliability
4. Safety & equipment protection
5. Efficiency & profitability
6. Operation during transitions
7. Dynamic Performance
8. Monitoring & diagnosis
Chapter 3 Flexibility
In the operating window, we
Selected controlled and manipulated variables
Determined the capacity of equipment
In the flexibility analysis, we
Added equipment to enable the system to respond to disturbances and changes to set points
In the upcoming reliability and safety, we
Add capacity and flexibility for atypical situations that can damage equipment and/or introduce hazards
In the upcoming process control, we
Finalize the strategies for using measurements to adjust final elements automatically achieve the all goals
Wrap-up and Look ahead

## Slide 51
Key Operability issues
1. Operating window
2. Flexibility/
controllability
3. Reliability
4. Safety & equipment protection
5. Efficiency & profitability
6. Operation during transitions
7. Dynamic Performance
8. Monitoring & diagnosis
Chapter 3 Flexibility
Citations
6. van Lieshout, Laurens (2019) https://commons.wikimedia.org/wiki/File:Steer_system.jpg
1. Castelnuovo, R. (2005) https://commons.wikimedia.org/wiki/File:Centrifugal_3.png#/media/File:Centrifugal_3.png
2. Duk (2005) https://commons.wikimedia.org/wiki/File:Gear_pump.png
3. Howitworks (2019) http://howitsworkss.blogspot.ca/2015/06/centrifugal-compressor.html
5. Smith, Glenda (2013) Compressor performance diagram: http://petrowiki.org/Centrifugal_compressor
4. Padleckas, H. (2006) https://commons.wikimedia.org/wiki/File:Straight-tube_heat_exchanger_2-pass.PNG